## Slide 2: Recall:

## Slide 4
The current in an ohmic conductor is proportional to the voltage across it, provided that the temperature and other physical conditions are kept constant.
Recall: Ohm’s Law
V = R × I
R is the resistance, measured in ohms (Ω).

## Slide 5: Equivalent resistance
When designing or analysing circuits, complex combinations of resistors are common. To perform calculations, for example to find a suitable fuse to protect the circuit, it is easier to use a value for the total resistance of the circuit, RT.
R1
R2
R3
R4
R5
R6
R7
RT
RT can be called the equivalent resistance because it is the single resistor that is equivalent to the complex combination.
Notes: Boardworks AS Physics
Resistance and Resistivity

## Slide 6: Resistors in series
To work out the equivalent resistance of resistors in series, the resistor values can just be added together:
In general for a number of resistors, n:
RT = R1 + R2 + … + Rn
10 Ω
20 Ω
15 Ω
equivalent resistance = 10 + 20 + 15
= 45 Ω
Notes: Boardworks AS Physics
Resistance and Resistivity

## Slide 7: Resistors in parallel
To work out the equivalent resistance for resistors in parallel, a more complex equation must be applied:
For example:
10 Ω
20 Ω
15 Ω
1
RT
=
+
+
…
+
1
R1
1
R2
1
Rn
=
1
RT
1
10
1
20
1
15
+
+
1
RT
=
60
6 + 3 + 4
1
RT
=
13
60
=
RT
60
13
= 4.62 Ω
Ω
Notes: Teacher notes
If students struggle with the maths in this example, they could be reminded that to add fractions together, you should first find the lowest common denominator, in this case 60.
Boardworks AS Physics
Resistance and Resistivity

## Slide 8: Resistor combinations
Notes: Teacher notes
Students could be encouraged to draw a diagram for each question before beginning the calculation.
Boardworks AS Physics
Resistance and Resistivity

## Slide 9: Kirchhoff’s first law
Kirchhoff’s first law states that:
The sum of the currents leaving any junction is always equal to the sum of the currents that entered it.
The German physicist Gustav Kirchhoff established two laws which help us to understand the function of electric circuits.
This law is based upon the idea of the conservation of charge: no charge can be lost or made in a circuit.
Thus the sum of the currents at a junction should be zero.
IIN = I1 + I2 … + In
ΣI = 0
IIN
I3
I2
I1
Notes: Boardworks AS Physics
Simple Circuits

## Slide 11: The energy in a circuit
What happens to the energy supplied to a circuit?
Batteries and power supplies supply electrical energy to a circuit. Devices within the circuit change this energy to other forms: bulbs produce heat and light, resistors produce heat.
Energy cannot be created or destroyed. All of the energy provided by a power supply must be used by the circuit.
Voltage is the energy transferred to the charge in a circuit. The battery’s voltage is shared between the components, which changes this energy into different forms.
What is the conservation of energy?
How does the voltage of a battery relate to the voltage measured across the devices in a circuit?
Notes: Boardworks AS Physics
Simple Circuits

## Slide 12: Kirchhoff’s second law
Kirchhoff’s second law is based upon the law of the conservation of energy. It states that:
The total voltage across a circuit loop is equal to the sum of the voltage drops across the devices in that loop.
Essentially, the energy you put into the circuit equals the energy you get out of each circuit loop.
An equation can be produced for each loop in a circuit. For example:
VIN = V1 + V2
VIN = IR1 + IR2
R1
I
VIN
V2
V1
R2
Notes: Teacher notes
In this equation IR is derived from the equation V = I × R.
Boardworks AS Physics
Simple Circuits

## Slide 13: Further uses for Kirchhoff’s law
There are 3 loops in the circuit. Each has a voltage drop equal to the input voltage according to the 2nd law.
Use Kirchhoff’s laws to find the values for each current.
10 Ω
100 Ω
40 Ω
I1
I2
I3
I
E = 12 V
Therefore: I = I1 + I2 + I3
As I =
I =
12
10
100
40
12
12
+
+
I = 1.2 + 0.12 + 0.3
I = 1.6 A
I1 = 1.2 A
I2 = 0.1 A
I3 = 0.3 A
The 1st law means that current entering each junction equals the current leaving.
V
R
V3
V2
V1
Therefore: E = V1 = V2 = V3
Notes: Boardworks AS Physics
Simple Circuits