## Slide 1: Recall: Different forms of the power equation
Electrical power can also be calculated using resistance.
P = V × I
P = I2 × R
P = V2 ÷ R
and… V = I × R
P = V × I
Therefore, using substitution:
P = I × R × I
and… I = V ÷ R
P = V × V ÷ R
Therefore, using substitution:
The equations linking power to resistance are found by substituting the equation V = I × R into the power equation:

## Slide 2
Recall:
I = Q /t  Q = It
Therefore: Ep= I t V

## Slide 3: Efficiency
A light bulb converts electrical energy to useful light and wasted heat.
Efficiency is a measure of how well a device transforms energy into useful forms.
light
What is the efficiency of the bulb if it converts 50 J of electrical energy into 45 J of heat energy?
efficiency =
=
electrical
heat
× 100
useful energy out
total energy in
× 100
= 10 %
5
50

## Slide 4: Efficiency of a motor
What is the efficiency of this system, if the motor takes 5 seconds to lift the weight?
(take gravity to be 9.81 N/kg)
1.4 kg
1.5 m
6 V
2 A
motor
pulley
=
efficiency =
useful energy out
total energy in
× 100
energy into system:
electrical energy = I × t × V
= 2 × 5 × 6
= 60.0 J
energy used:
gravitational potential energy = m × g × h
= 1.4 × 9.81 × 1.5
= 20.6 J
60.0
= 34.3 %
20.6
× 100